## Slide 1: FMU Simulation Environment for Cyber-Physical Systems Co-Design Introduction & Use Case
David.Kaufmann@ist.tugraz.at

## Slide 2: Overview
Modeling in OpenModelica
Functional Mock-up Unit (FMU) Standard
FMU Simulation Environment
Use Case Heater Model
ASP Diagnose Tool
FMU Simulation Environment for Cyber-Physical Systems Co-Design

## Slide 3: Modeling in OpenModelica
FMU Simulation Environment for Cyber-Physical Systems Co-Design
OMEdit editor for creating models
Use Linux pre-built OpenModelica VirtualBox:
  Link to Linux VB release
Model the system according to OpenModelica standard
Input
  Define inputs with “input” statement to have access in FMU model.
Output:
  All used variables can be read as output signals.

## Slide 4: Modeling in OpenModelica
FMU Simulation Environment for Cyber-Physical Systems Co-Design
Co-Simulation:
FMUs contain local solvers
Enables step by step simulation
Export FMU:

## Slide 5: Functional Mock-up Unit (FMU)
The Functional Mock-up Interface (or FMI) defines a standardized interface to be used in computer simulations to develop complex cyber-physical systems.
FMI defines an interface that is implemented by an executable called a Functional Mock-up Unit (FMU)
An FMU contains following:
A model description XML file:
  Model information.
  Variable definitions as type, unit and description.
  General model information as name, generation tool and FMI version.
Model equations:
  Differential equations, algebraic relations and discrete equations.
  Represented in C functions and binaries.
FMU Simulation Environment for Cyber-Physical Systems Co-Design

## Slide 6: FMU Simulation Environment General Idea
FMU Simulation Environment for Cyber-Physical Systems Co-Design
Provide user friendly simulation environment for FMUs.
Enable a step-by-step simulation (Co-Simulation FMU).
Enable coupling of multiple simulated FMU models.
Build a client server environment to access from different programming environments (Python or Java).
Dockerise simulation environment as server with a REST API.
Provide a client interface to communicate with the server.
Provide signal chart drawing.
Clone Gitlab repository:
  git clone https://ss22_mts:x-sykzfA_Ld1PVArrwsz@git.ist.tugraz.at/MBR/AI4DI/fmu_simulation_environment
Server
FMU
Client
REST
HTML
Signal plotting
Simulation
Control Simulation

## Slide 7: FMU Simulation Environment Client Server Setup
FMU Simulation Environment for Cyber-Physical Systems Co-Design

## Slide 8: FMU Simulation Environment Configure and Upload Simulation Model
FMU Simulation Environment for Cyber-Physical Systems Co-Design

## Slide 9: FMU Simulation Environment Model Configuration Structure
FMU Simulation Environment for Cyber-Physical Systems Co-Design
Init Inputs
Configuration
Pre-defined input changes
Signal Output
Timestep Size
Config-File
Server address
FMU file path

## Slide 10: Use Case Heater Model
FMU Simulation Environment for Cyber-Physical Systems Co-Design
Heater FMU
Heater CONFIG
Heater Simulation Controller
Start Heater Model Docker Container
Name: model
Address: localhost:81
heater_intern_control.py
config_heater_model.json
heater_model.fmu
Simple Heater Model
  First order differential equation
  Heater panel to heat up a medium
  Surrounding environment with a global ambient temperature
  Constant heat capacitance,
  Constant heat transfer coefficient
  Medium temperature is observed
Temperature Control Unit
  External placed 2-point controller

## Slide 11: Use Case Heater Model
FMU Simulation Environment for Cyber-Physical Systems Co-Design
Build Docker Image
Start Docker Container
  Name
  Address & port
Simulation Controller
  Initialize
    Communication interface (server address)
    Upload FMU model to server
    Upload Configuration file
  Trigger simulation update by given timestep
  Get output signals and send to 2-point control unit
  Get 2-point control unit output and send as input signal to server
LIVE DEMO

## Slide 12: ASP Diagnose Tool
ASP Diagnose Tool
Clone Gitlab Repository:
  git clone https://ss22_mts:-ZbnH7jrYe3JzrT1dod9@git.ist.tugraz.at/MBR/AI4DI/asp_clingo_python_tool.git
Answer Set Programming (ASP) model diagnose tool
Theorem solver: Clingo 5.4.1
Modeling cyber physical systems in ASP
Searching for abnormal behavior of components
Setup options:
  ASP File or directory to perform diagnose
  Number of required answersets
  Definition of fault size (e.g.: 2 -> 0 (as reference), 1, 2 searched)
  Automatic constraint adding after each diagnose run
  Additional observation file
Result options:
  Terminal
    file, fault size, observations, diagnose, time for diagnose
  JSON
    index, file, fault size, observations, diagnose, time for diagnose
  CSV
    index, file, time for diagnose, number of diagnosis found, total time
ASP Models
Diagnose Tool
Search for abnormal component behavior
JSON
CSV
Options
Answersets
Fault size
Observations
…
Results
Terminal
JSON
CSV

## Slide 13: Thank you for your attention!
David.Kaufmann@ist.tugraz.at